## Slide 1
(GIS-based approach) Exploration of individual potential sites by the nine land-use types
(Geographical constraint)
Slope : (Mountainous area) below 15˚
Protected Area : (Farmland) 농업보호구역, 농업진흥지역; (Mountainous area) 보전산지
Setback distance : All land-use types; different policy by cities and counties
Parameters based on observed PV installation sites data.
Ratio : Area covered by PV panel to the total area (%)
Coefficient : Required area(m2) to install PV (1kW)
Capacity factor : The ratio of the expected annual average energy production
to the annual energy production assuming the plant operates at its rated capacity
every hour of the year (%)
LCOE by cities and counties
LCOE by PV technology types
Equation
3. Calculate PV potential
4. Derive supply curve for PV
2. Explore PV-available sites
1. Categorize Land-use & PV type
Classification considering policy design for PV deployment :
PV technology types (a, b, c) & Land-use types (1-9) as followings;
(a) roof-top PV : (1) Industrial complex, (2) Logistics complex, (3) Residential complex, (4) Public buildings
(b) ground-mounted PV : (5) Mountainous area, (6) Farmland, (7) Parking lot, (8) Roadside land
(c) floating PV : (9) Water
No Regulation
All is available
Regulation
내용입력 : 내용을 입력해주세요
Scenario
No Setback
Scenario
Setback

## Slide 2
Installed capacity of PV (kW)
PV installation Area (m2)
Slope : 11.50
Slope : 7.23

## Slide 3
Installed capacity of PV (kW)
PV installation Area (m2)
Slope : 11.50
Slope : 7.23

## Slide 4
경기 시흥시 옥구천서로131번길 15 시화단지 1라 503호(정왕동)
(a)
(b)

## Slide 5
PV installation Area (m2)
Total Area (m2)
Slope : 0.545
Slope : 0.189
Slope : 0.284

## Slide 6
PV installation area (m2)
Total area (m2)
Slope : 0.545
Slope : 0.189
Slope : 0.284

## Slide 7
Categorize Land-use & PV technology Type
Classification considering policy design for PV deployment:
Land-use types : (1) Industrial complex, (2) Logistics complex, (3) Residential complex, (4) Public buildings, (5) Mountainous area, (6) Farmland, (7) Parking lot, (8) Roadside land, (9) Water
Geographical constraint
Slope, Protected Area, Setback distance
Parameters calculated using observed PV sites data.
(1) Ratio : Area covered by PV panel to the total area (%)
(2) Coefficient : Required area(m2) to install PV (1kW)
(3) Capacity factor : Expected annual average energy production divided by the annual energy production assuming the plant operates at rated capacity for every hour of the year.
내용을 입력해주세요
내용을 입력해주세요
Calculation parameter
2020
PV technology types: (1-4) roof-top PV, (5-8) ground-mounted PV, (9) floating
GIS-based approach
Exploration of individual potential sites in Gyeonggi province by the nine land-use types
Slope, Protected Area, Setback distance

## Slide 8
Categorize Land-use & PV technology Type
Classification considering policy design for PV deployment :
PV technology types (a, b, c) & Land-use types (1-9) as followings;
(a) roof-top PV : (1) Industrial complex, (2) Logistics complex, (3) Residential complex, (4) Public buildings
(b) ground-mounted PV : (5) Mountainous area, (6) Farmland, (7) Parking lot, (8) Roadside land
(c) floating PV : (9) Water
Parameters calculated using observed PV sites data.
(1) Ratio : Area covered by PV panel to the total area (%)
(2) Coefficient : Required area(m2) to install PV (1kW)
(3) Capacity factor : The ratio of the expected annual average energy production
to the annual energy production assuming the plant operates at its rated capacity every hour of the year (%)
Assume parameter
LCOE
Explore every sites using GIS-based approach
Exploration of individual potential sites in Gyeonggi province by the nine land-use types
Apply geographical constraint
Slope : (Mountainous area) below 15˚
Protected Area : (Farmland) 농업보호구역, 농업진흥지역; (Mountainous area) 보전산지
Setback distance : All land-use types; different policy by cities and counties
Calculate potential for PV
P
Parameters calculated using observed PV sites data.
(1) Ratio : Area covered by PV panel to the total area (%)

## Slide 9
Categorize Land-use & PV technology Type
Classification considering policy design for PV deployment :
PV technology types (a, b, c) & Land-use types (1-9) as followings;
(a) roof-top PV : (1) Industrial complex, (2) Logistics complex, (3) Residential complex, (4) Public buildings
(b) ground-mounted PV : (5) Mountainous area, (6) Farmland, (7) Parking lot, (8) Roadside land
(c) floating PV : (9) Water
Explore every sites using GIS-based approach
Exploration of individual potential sites in Gyeonggi province by the nine land-use types
Apply geographical constraint
Slope : (Mountainous area) below 15˚
Protected Area : (Farmland) 농업보호구역, 농업진흥지역; (Mountainous area) 보전산지
Setback distance : All land-use types; different policy by cities and counties
Parameters calculated using observed PV sites data.
(1) Ratio : Area covered by PV panel to the total area (%)
(2) Coefficient : Required area(m2) to install PV (1kW)
(3) Capacity factor : The ratio of the expected annual average energy production
to the annual energy production assuming the plant operates at its rated capacity
every hour of the year (%)
Assume parameter for calculating potential
Calculate potential for PV
P
LCOE by cities and counties
LCOE by PV technology types
Assume parameter for calculating LCOE
Calculate potential for PV
P

## Slide 10
2.1 Explore every sites using GIS-based approach
Exploration of individual potential sites in Gyeonggi province by the nine land-use types
2.2 Apply geographical constraint
Slope : (Mountainous area) below 15˚
Protected Area : (Farmland) 농업보호구역, 농업진흥지역; (Mountainous area) 보전산지
Setback distance : All land-use types; different policy by cities and counties
Parameters calculated using observed roof-top PV sites data.
(1) Ratio : Area covered by PV panel to the total area (%)
(2) Coefficient : Required area(m2) to install PV (1kW)
(3) Capacity factor : The ratio of the expected annual average energy production
to the annual energy production assuming the plant operates at its rated capacity
every hour of the year (%)
3.1 Assume parameter for calculating potential
3.2 Calculate potential for PV
Equation??
LCOE by cities and counties
LCOE by PV technology types
4.1 Assume parameter for calculating LCOE
3. Calculate PV potential
4. Derive supply curve for PV
Equation??
4.1 Assume parameter for calculating LCOE
2. Explore PV-available sites
1. Categorize Land-use & PV type
Classification considering policy design for PV deployment :
PV technology types (a, b, c) & Land-use types (1-9) as followings;
(a) roof-top PV : (1) Industrial complex, (2) Logistics complex, (3) Residential complex, (4) Public buildings
(b) ground-mounted PV : (5) Mountainous area, (6) Farmland, (7) Parking lot, (8) Roadside land
(c) floating PV : (9) Water

## Slide 11
2.1 Explore every sites using GIS-based approach
Exploration of individual potential sites in Gyeonggi province by the nine land-use types
2.2 Apply geographical constraint
Slope : (Mountainous area) below 15˚
Protected Area : (Farmland) 농업보호구역, 농업진흥지역; (Mountainous area) 보전산지
Setback distance : All land-use types; different policy by cities and counties
Parameters calculated using observed PV installation sites data.
(1) Ratio : Area covered by PV panel to the total area (%)
(2) Coefficient : Required area(m2) to install PV (1kW)
(3) Capacity factor : The ratio of the expected annual average energy production
to the annual energy production assuming the plant operates at its rated capacity
every hour of the year (%)
LCOE by cities and counties
LCOE by PV technology types
Equation
3. Calculate PV potential
4. Derive supply curve for PV
2. Explore PV-available sites
1. Categorize Land-use & PV type
Classification considering policy design for PV deployment :
PV technology types (a, b, c) & Land-use types (1-9) as followings;
(a) roof-top PV : (1) Industrial complex, (2) Logistics complex, (3) Residential complex, (4) Public buildings
(b) ground-mounted PV : (5) Mountainous area, (6) Farmland, (7) Parking lot, (8) Roadside land
(c) floating PV : (9) Water